## Slide 1: Networking Setup
The following pages show several networking configurations, in increasing order of capability
Goals:
  To use normal home networking equipment (consumer-grade routers, switches and access points) you can get at the normal electronics outlets
  To limit configuration to what a regular hobbyist normally does (set the Wi-Fi names, open gaming ports)
Notes:
  The Internet addresses used don’t matter. The ones used are realistic, but yours will most likely be different.

## Slide 2
10.0.0.234
192.168.0.1
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
192.168.0.100:8080
Main Router
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
Simplest setup
One main router
WAN can connect to internet if needed.
Connections are Wi-Fi
  But the main laptop should be wired
Optionally, you can also wire the announcer, etc.
Physical or WIFI connection
IP Connection

## Slide 3
10.0.0.234
192.168.0.1
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
192.168.0.100:8080
Main Router
Switch for additional ports
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
Wired setup (bad Wi-Fi or long distances)
One main router
WAN can connect to internet if needed.
For remote or dead spots
Connect a switch to the router, or
Connect an access point to the router, or
Connect a router to the router (see next page)
Additional Access Point
Physical or WIFI connection
IP Connection

## Slide 4
10.0.0.234
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
WAN
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform or room
LAN 2 192.168.1.165
Distant room using routers
You can connect a router to any of the LAN ports
On the secondary router(s)
  For simplicity use different names for each Wi-Fi networks
  Ideally, change the Wi-Fi channel to be different
This should work “plug and play”
Physical or WIFI connection
IP Connection

## Slide 5
10.0.0.234
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Owlcms DHCP Reservation 192.168.0.100:8080
WAN
WAN
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
Switch for additional ports
Switch for additional ports
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform or room
LAN 2 192.168.1.165
Multiple platforms
One secondary router per additional platform, connected to the main router.
Use different Wi-Fi names and different channels for each platform
You can still connect one or more switches or access points to each router if you need more ports.
Additional Access Point
Physical or WIFI connection
IP Connection

## Slide 6
107.171.217.85
10.0.0.234
10.0.0.1
192.168.0.1
192.168.0.240
Wi-Fi 2 192.168.1.115
Internet Router
Owlcms DHCP Reservation 192.168.0.100:8080
OBS
WAN
WAN
WAN
10.0.0.234:8080 port redirection configured on router 1 for 192.168.0.100:8080
192.168.0.100:8080 (via default gateway)
Main Router
Secondary Router
Switch for additional ports
Switch for additional ports
192.168.1.1
Wi-Fi 1 192.168.1.122
LAN 1 192.168.0.110
Heroku publicresults
YouTube Facebook streaming
Competition Network
All machines see owlcms using its 192.168 address
One secondary router per additional platform
LAN 2 192.168.1.165
Additional Access Point
Physical or WIFI connection
Isolated Video Network
Needs a redirection to see owlcms
Avoids video traffic hitting the competition router
IP Connection

## Slide 7
10.0.0.232
Bridge Wi-Fi (Routeur B)
Owlcms DHCP Réservation 192.168.0.139:8080
OBS
10.0.0.120
192.168.0.1
WAN
Port externe 8080 redirection vers 192.168.0.139:8080
Routeur A
Heroku publicresults
YouTube Facebook streaming
Réseau de compétition
Même configuration et adresses réseau que normalement
Toutes les antennes WiFi vont dans les ports PoE
Tous les appareils câblés vont dans les commutateurs (switch)
Configuration du routeur (« redirection ») pour permettre l’accès à partir de OBS
WiFi Access Point
Connexion ethernet ou wifi
Réseau pour transmission vidéo
Logiciel OBS pour superposer vidéo et données de compétition (athlète courant, poids demandé, etc.)
Pont WiFi pour se brancher au réseau
Permet aussi de publier les résultats sur le cloud
Connexion logique IP
WiFi Access Point
Switch supplémentaire pour plateforme 2
X
Commutateur (Switch) Power over Ethernet (PoE)
PoE
PoE
Wi-Fi Public

## Slide 8
10.0.0.232
Vidéo
Owlcms DHCP Réservation 192.168.0.139:8080
OBS
10.0.0.120
192.168.0.1
WAN
Port externe 8080 redirection vers 192.168.0.139:8080
Competition
Heroku publicresults
YouTube Facebook streaming
Réseau de compétition
Même configuration et adresses réseau que normalement
Toutes les antennes WiFi vont dans les ports PoE
Tous les appareils câblés vont dans les commutateurs (switch)
Configuration du routeur (« redirection ») pour permettre l’accès à partir de OBS
Connexion ethernet ou wifi
Réseau pour transmission vidéo
Logiciel OBS pour superposer vidéo et données de compétition (athlète courant, poids demandé, etc.)
Pont WiFi pour se brancher au réseau
Permet aussi de publier les résultats sur le cloud
Connexion logique IP
Commutateur (Switch)
X

## Slide 9
10.0.0.232
Video Router
Owlcms DHCP Reservation 192.168.0.100:8080
OBS
10.0.0.120
192.168.0.1
WAN
External port 8080 redirection to 192.168.0.100:8080
Competition Router
Heroku publicresults
YouTube Facebook streaming
Competition network
Same configuration you would normally use
All cabled computers are on the switch. Critical computers are cabled.
One port is open to the outside to allow OBS to reach owlcms
Ethernet or WiFi
Video network
Does not interfere with competition
Cabled out or WiFi bridge
Logical IP connection
Commutateur (Switch)
X

## Slide 10
10.0.0.232
WiFi Bridge
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
Commutateur (Switch)
scoreboards
camera
Facility WiFi
WiFi Access Point
PoE
Critical computers are cabled (announcer, marshall) or close to wifi access point. Use multiple APs as required.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
Separate WiFi Access Points, Video Broadcast using Facility WiFi
X
X

## Slide 11
Owlcms
OBS
107.171.217.85
192.168.0.1
WAN
Competition Router
Heroku publicresults
Video streaming
WiFi Access Point
Physical or WIFI connection
IP traffic
WiFi Access Point
Additional switch for platform 2
X
PoE-capable Switch (one per platform)
PoE
PoE
scoreboard
Large venue setup
Main laptop is on a wired connection on the first platform switch
One platform = one switch
Power over Ethernet for redundant WiFi Access Points
Other platform switches connect directly to main switch
Announcer, ref console can be wired if desired using free ports
No interference from video traffic
Router
Provides DHCP addresses
Allows OBS to fetch scoreboards from owlcms
Allows OBS to stream out
Allows owlcms to feed Heroku public scoreboards

## Slide 12
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
scoreboards
camera
Critical computers are cabled (announcer, marshall) or close to wifi access point.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
WiFi Router only, OBS Broadcast using Facility Wired Connection
Facility Network

## Slide 13
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
Commutateur (Switch)
scoreboards
camera
PoE
Critical computers are cabled (announcer, marshall) or close to wifi access point. Use multiple APs as required.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
WiFi Router, External Switch, OBS Broadcast using Facility Wired Connection
Facility Network

## Slide 14
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku publicresults
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
Commutateur (Switch)
scoreboards
camera
Facility Network
WiFi Access Point
PoE
Critical computers are cabled (announcer, marshall) or close to wifi access point
Only video and external scoreboard update traffic goes through the router
Second external switch used to keep all traffic local to the switch
data entry, scoreboards
Separate WiFi Access Points, OBS Broadcast using Facility Wired Connection
X

## Slide 15
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
scoreboards
camera
Critical computers are cabled (announcer, marshall) or close to wifi access point.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
WiFi Router only, OBS Broadcast using Facility WiFi
10.0.0.232
WiFi Bridge
Facility WiFi
X

## Slide 16
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
Commutateur (Switch)
scoreboards
camera
PoE
Critical computers are cabled (announcer, marshall) or close to wifi access point. Use multiple APs as required.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
WiFi Router, External Switch, OBS Broadcast using Facility WiFi
10.0.0.232
WiFi Bridge
Facility WiFi
X

## Slide 17
10.0.0.232
WiFi Bridge
Owlcms 192.168.0.100
OBS
10.0.0.120
192.168.0.1
WAN
Competition Router
Heroku public results
YouTube Facebook streaming
Competition network
Ethernet or WiFi
Logical IP connection
Commutateur (Switch)
scoreboards
camera
Facility WiFi
WiFi Access Point
PoE
Critical computers are cabled (announcer, marshall) or close to wifi access point. Use multiple APs as required.
External switch is used to keep all traffic local to the switch, no dependency on router other than DHCP
WiFi done using access point, only video traffic goes through the router. Router WiFi turned off.
data entry, scoreboards
Separate WiFi Access Points, OBS Broadcast using Facility WiFi
X
X